GUC Series Mine Safety Type Displacement Sensors

Applications

Hydraulic Roof Supports

Roadheaders

Features

◆Intrinsically safe products meet GB3836-2010 MT1109-2011 and Q / XKYC 14-2012 standard, get ​​coal safety certificate. Explosion-proof mark：ExibI;

◆Contactless Sensing with Highest Durability;

◆Installed in the hydraulic cylinder, the absolute value of the output;

◆Material and electrical performance conforms to mine safety requirements, high security;

Specifications

◆GUC1200(A) Series

Security parameters：Ui：12.5V  Ii：15mA  Ci：0uF  Li：0mH

Operating voltage：+12V DC±10%

Current drain：≤15mA DC

Output: DC （0.5～4.5V）±0.02V； Load : 2KΩ～∞

Non-linearity: <±0.1%F.S.

Repeatability:<±0.01%F.S.

Resolution: 12bitD/A , 0.17mm

Measuring range: ：0~1200mm

◆GUC1200(B) Series

Security parameters：Ui：12.5V  Ii：15mA  Ci：0uF  Li：0mH

Operating voltage：+12V DC±10%

Current drain：≤10mA DC

Output: DC （0.5～4.5V）； Load : 2KΩ～∞

Non-linearity: <±0.2%F.S.

Repeatability:<±0.01%F.S.

Resolution: 10bitD/A , 1mm

Measuring range: 0~1200mm

◆GUC1200/2440(C) Series

Security parameters：Ui：12.5V  Ii：15mA  Ci：0uF  Li：0mH

Operating voltage：+12V DC±10%

Current drain：≤20mA DC

Output: DC （0～5V）； Load : 2KΩ～∞

Non-linearity: <±0.2%F.S.

Repeatability:<±0.01%F.S.

Resolution: 16bitD/A , 0.34mm

Measuring range: 0~1200mm, 0~2440mm

Application Overview:

GUC series of mine safety type displacement sensor apply to Hydraulic Roof Supports, Roadheaders and other mining equipment, the user can choose according to the actual installation structure.

Ordering Information:

GUC1200(A)、GUC1200(B)、GUC1200/2440(C)  (Please specify the scale procurement.)

Product Diagram:

GUC1200(A)

GUC1200(B)

GUC1200/2440(C)

Application Picture:

Hydraulic Roof Supports  								Roadheaders

# Text boxes

Xinhui KangYu Control Systems Engineering, Inc.

Guifeng Hightech Village, Ximen Rd., Xinhui District, Jiangmen City, Guangdong 529100, P.R. China

Tel: 86-750-6318857	 Fax: 86-750-6318900  E-mail: sale@chinakangyu.com  Website: www.chinakangyu.com

Description

GUC series of mine safety type displacement sensor is a magnetostrictive principle of non-contact absolute position measurement of displacement sensors, suitable for a mixture of methane gas and coal dust explosion hazards of coal mine. Contactless sensing with highest durability, Stable and reliable performance. Operating ambient temperature can work normally in the range of -10 ℃ to 60 ℃. Excellent performance of the sensor, allowing users ease of use.